# GLOSSARY OF TERMS

| Allowable Load – Mechanical (ALm) | The maximum allowable load on a structural element as specified by its manufacturer. ALm is usually limited to 50% of the Rated Ultimate Mechanical Capacity. |
| --- | --- |
| Allowable Load – Geotechnical (ALg) | The maximum allowable load that may be transferred into a Helical Screw Pile Foundation as determined by the geotechnical properties of the soil. Usually determined by load test behavior or engineering analysis. ALg is typically limited to 50% of the Ultimate Geotechnical Capacity of the pile, but this may vary, depending on project parameters and other factors. |
| Creep | The continuous deflection (movement) of a pile while subjected to a constant load. |
| Crowd | Axial compressive force applied to the helical anchor as needed to ensure that the anchor progresses into the ground a distance equal to the helix pitch for each revolution. |
| Dead Load | Loads resulting from the weight of the structure plus all material (equipment) permanently fastened thereto or supported thereby. |
| Design Load (DL) | The maximum load that will be transferred to the pile. The Design Load is expressed in terms of magnitude and direction. Design Loads can be Tensile, Compressive or Lateral. Also known as Service Load and Working Load. |
| Effective Torsional Resistance | Effective Torsional Resistance is used to estimate Ultimate Geotechnical Capacity of a pile during construction. Helical Screw Pile Foundations are typically installed to a predetermined Specified Installation Torque. |
| Factor of Safety | See Safety Factor. |
| Failure – Geotechnical | Unless otherwise noted, geotechnical failure is achieved when continuous deflection (movement) of a pile occurs while subjected to a constant load. i.e. When creep occurs. |
| Foundation | An element that connects a structure to the earth. Loads are transferred from the structure, to the foundation, to the earth. These loads can be Compression, Tension, Lateral or Dynamic. |
| Geotechnical Capacity | The maximum load that can be resisted via the bearing of helical plates on the soil and skin friction or adhesion between the soil and shaft in which the pile is embedded. |
| Helical Extension | Same as a Plain Extension, but with one or more helices welded to it. Used in areas of very weak soils or as an onsite modification when unexpected weak soils are encountered. The Helical Extension is attached directly above the Helical Lead section or sometimes above other helical extensions. |
| Helical Lead Section | A central Shaft with one or more Helices welded to it. The first component of a Helical Screw Pile Foundation that enters the soil. Extensions are used in conjunction with the Helical Lead Section to achieve the specified depth and to enter competent soil. |
| Helix | Generally a rounded steel plate formed into a helical flight. When rotated in the ground, the helical shape provides thrust along its longitudinal axis thus aiding in the anchor installation, plus the plate transfers axial load to the soil through bearing after installation. |
| Live Load | Loads resulting from vehicles, people, snow, ice, wind, and impact. Other forces resulting from earthquakes and other extraordinary conditions. |
| Load Test | Determining capacity and relation of load to movement by applying incremental loads to the helical screw pile. Engineers, to determine Allowable Load, often apply the results of load tests. See Proof Test. |
| Mechanical Strength | See Rated or Ultimate Mechanical Capacity |
| Nominal Load | See Design Load |
| Plain Extension | A central shaft (with no helices) that is attached directly above the helical lead section. Extensions are coupled together and are used to extend the helical lead section to a required depth and into a soil stratum of suitable strength. |
| Proof Test | Load testing a Helical Screw Pile Foundation by applying loads in predetermined increments, maintaining each load for a period of time and recording deflection at the beginning and end of each increment. Engineers, to determine Allowable Load, often apply the results of proof tests. |
| Rated or Ultimate Mechanical Capacity | The Ultimate Mechanical Capacity of a structural element as specified by its manufacturer. Determined by load tests and/or engineering analysis. Also referred to as Mechanical Strength. |
| Rated or Ultimate Torsional Strength | The maximum torque that can be safely applied to a Helical Screw Pile Foundation during installation. |
| Reveal | The distance from the ground surface to the upper end of the last installed extension of an anchor, measured along the anchor’s longitudinal axis. |
| Safety Factor (SFg) - Geotechnical | The ratio of the Ultimate Geotechnical Capacity (UCg) of a Helical Screw Pile Foundation to the Design Load. |
| Safety Factor (SFm) - Mechanical | The ratio of the Rated Ultimate Mechanical Capacity of a structural element to the Design Load. |
| Service Load | See Design Load |
| Shaft | The central shaft of a Helical Screw Anchor used to transfer load from the structure to the bearing plate/s (helices). Shafts may be solid square steel bar or hollow steel pipe sections. Shaft sizes typically range from 1.25” to 2.00” square, and from 2.875” to 10.75” diameter hollow round. |
| Specified Installation Torque | The Effective Torsional Resistance to be achieved - as specified by the engineer. |
| Ultimate Pile Capacity - Geotechnical (UCg) | The maximum load that can be applied to a Helical Screw Pile Foundation prior to geotechnical failure. At this point no additional capacity can be justified. |
| Ultimate or Rated Pile Capacity - Mechanical (UCm) | The manufacturers’ Rated Ultimate Mechanical Capacity of the Helical Screw Pile Foundation. |
| Ultimate Pullout Resistance | Limit state based on the lesser of mechanical strength or geotechnical capacity of the helical anchor - defined as the point at which no additional axial tension load can be justified. |
| Working Load | See Design Load. |